## Slide 1: MazY
Steve Mahar
Peter Tuerk

## Slide 2: What Is MazY?
Line Following Robot
Controlled By An Android App
Our Goals
  Explore Mazes
  Optimize Routes

## Slide 3: MazY’s Hardware
Raspberry Pi B+
Bluetooth Dongle
2 Leggo Motors
L298N Motor Controller
2 Custom Optical Line Sensors

## Slide 4: MazY’s Software
Raspian
Bluez
BCM2835 GPIO Library
GromOS
  Connects With Android Phones
  Provides An Easy Shell
  Provides An Application Interface For Robotics

## Slide 5: The Maze
3 Simple Rules
  Only Straight Lines
  Intersections Must Be 4 Way
  Dead Ends Must Have T’s

## Slide 6: Our Application
Discover Mazes
  Uses All Sensors
  Each New Intersection Adds A Node On The Stack
  Each Dead End Modifies The Value On Top Of The Stack
  3 Dead Ends Pops A Node Off The Stack
Solve Mazes
  Uses The Previously Generated Stack
  Uses Time Based Turns
  Each Intersection Pops One Node off the Stack

## Slide 7: The User Interface
Send List Items To The Android Phone
Message Handler To Receive User Input
Main Menu
  Discover
  Solve

## Slide 8: The Stack
Simple Linked List Than Holds Integers
  0 = Left
  1 = Straight
  2 = Right
Can Modify The Top Value

## Slide 9: State Machines
3 State Machines
  UI State Machine
  Discover State Machine
  Solve State Machine
Switch Cases

## Slide 10: Timers
The Raspberry Pi Does Not Have An Internal Clock
We Are Timing CPU Cycles Given To Us By The Operating System

## Slide 11: GPIO
All Digital Pins
Sensors Are Either Black Or White
Motors Are On Or Off

## Slide 12: How We Could Have Improved
5V Motors With A 5V Regulator
Better Optical Sensors
More Optical Senors
Rotation Sensor
Accelerometer
Camera?

## Slide 13: What We Learned
Robotics Is Hard
Hardware Limits Software
Modern IDEs Are Much Better Than Makefiles
You Have To Pay Attention When You’re On The Linux Command Line